Christopher Bero
Homework 3
CPE 495

Concept Evaluation & Design Expression Approaches

Problem 1: [40 points] Consider the problem that was solved using the Analytical Hierarchy Process, AHP, in Section 4.3.3 of the text. Assume that the following four criteria, accuracy, cost, size and availability, were evaluated resulting in the following pairwise comparison matrix.
	Accuracy	Cost	Size	Availability
Accuracy	1	1/3	2	1 / 2
Cost	3	1	5	1
Size	1 / 2	1 / 5	1	2
Availability	2	1	1 / 2	1

Assume that three candidate solutions have been developed (bipolar junction transistor, op amp, and current mirror) as shown in Figure 4.6.
- The SPICE circuit simulation accuracy analysis (assuming 10% resistors) in terms of output voltage deviation (maximum deviation from nominal) for the three designs is as follows : bipolar junction transistors (BJTs)=9.2%, op amps = 1.3%, and current mirror (RTD) = 1.9%. (You may use Equation 1 chapter 4, page 78 to obtain normalized ratings.)
- The parts costs are the following: resistors =$0.05, bipolar junction transistors (BJTs)=$0.10, op amps = $0.35, and current mirror (RTDs) = $0.25
- The Printed Circuit board area required for each design is as follows: bipolar junction transistors (BJTs)= 1 in2 op amps )= 1.56 in2, and current mirror (RTDs) = 2.25 in2. (You may use Equation 1 chapter 4, page 78 to obtain normalized ratings.)
- That availability of parts is as follows: resistors=99%, bipolar junction transistors (BJTs)=90%, op amps = 85%, and RTDs=70%.
Compute the rankings of the design options using a weighted decision matrix of the type shown in Table 4.6 of the text.

Criteria Weightings
	Accuracy	Cost	Size	Availability	Sum	Weight
Accuracy	1	1/3	2	1 / 2	125	0.186
Cost	3	1	5	1	300	0.447
Size	1 / 2	1 / 5	1	2	111	0.165
Availability	2	1	1 / 2	1	135	0.201

Scores
	Single BJT	Op Amp	Current Mirror	Weight
Accuracy	0.08	0.55	0.37	0.186
Cost	0.41	0.25	0.33	0.447
Size	0.48	0.31	0.21	0.165
Availability	0.31	0.33	0.35	0.201
Score	0.339	0.331	0.321

Problem 2: [10 points] Identify the major differences between the Analytical Hierarchy Process and the Pugh Selection Process.

The Pugh Selection Process differs from the Analytical Heirarchy Process in that is uses a simpler scoring method and is an iterative process.

Problem 3: [10 points] Compare and contrast top-down and bottom–up functional design methods.

Bottom up design begins with basic components and generates the overall system with them. Conversely, top down approaches begin with the overall system and then partition it into subtasks that work together to create the final system. Each subtask or subsystem is then refined and partitioned.

Problem 4: [10 points] Define in your own words the concepts of cohesion and coupling in functional designs.

Coupling refers to the number of data paths between subsystems. Cohesion refers to the design integrity and purpose of the subsystem; more cohesive systems require less coupling and have more direct output.

Problem 5: [10 points] Answer Problem 6.5 page 131 of text.

S0: ($0.00)
- Input Nickle → S1
- Input Dime → S2
- Input Quarter → S5

S1: ($0.05)
- Input Nickle → S2
- Input Dime → S3
- Input Quarter → S6

S2: ($0.10)
- Input Nickle → S3
- Input Dime → S4
- Input Quarter → S7

S3: ($0.15)
- Input Nickle → S4
- Input Dime → S5
- Input Quarter → S8

S4: ($0.20)
- Input Nickle → S5
- Input Dime → S6
- Input Quarter → S9

S5: ($0.25)
Return $0.00
→ S0

S6: ($0.30)
Return $0.05
→ S0

S7: ($0.35)
Return $0.10
→ S0

S8: ($0.40)
Return $0.15
→ S0

S9: ($0.45)
Return $0.20
→ S0

Problem 6: Answer Problem 6.9 [20 points] (note ‘do statements’ are the same thing as for loops in C++ or Java – you can use this notation) and either Problem 6.11 page 133 of text or problem 6.12 page 134 of text.

a)
while (X)
Y;

b)
do {
Y;
} while (X);

c)
if (A) {
if (B) {
…
} else {
…
}
} else {
if (C) {
…
} else {
…
}
}

Problem 6.12
	Customer / Measurements	Customer Info	Employee Info	Tubing Info	Frame Info
Customer / Measurements		Belongs to one			Has one
Customer Info	Has many
Employee Info					Has many
Tubing Info					Has many
Frame Info	Belongs to one		Has one	Has many