Christopher Bero
CPE 412
Homework 5

Create a hybrid multi-threaded/message passing implementation of the matrix/matrix multiplication program as outlined in Question 3 of Exam 2 and measure its execution characteristics on the UAH Jetson cluster. This representation assumes that the first matrix is of size lxm and the second matrix is of size mxn. Assume that the quantities being multiplied are of type float. This program should be written in a general manner to allows the number of message passing processes and the number of threads per message passing process to be independently set by the user at run time. The program should have been designed using the same row-wise decomposition method that was used in two of the previous homework assignments. It should be written in a manner that will result in the total amount of computation to be divided as evenly as possible among the message-passing processes with the computation that is assigned to each message-passing processes in turn being further divided as evenly as possible between the associated threads. A combination of MPI and either OpenMP or pThreads should be utilized to complete this problem. The number of threads should be a command-line parameter while the number of message-passing processes should be set using the mpirun command. The l, m, and n dimensions should also be command line parameters that can be set at run time. If the executable is named mm_mult_hybrid then the syntax needed to execute the code should take on the general form shown below:
mpirun -np [No. Processes] mm_mult_hybrid [No. Threads/Process] [dim_l] [dim_m] [dim_n])
After verifying that the program executes correctly on the Jetson cluster as discussed in class then comment out the output and record the execution times for the 1 MPI Process/8 thread per process case, 2 MPI Process/4 thread per process case, 4 MPI Process/2 thread per process case, and the 8 MPI Process/1 thread per process case assuming square matrices of size m=n=l=3,000. Also run a reference 1/MPI Process 1 thread per process case as a reference for the same m=n=l=3,000 dimensions. In collecting this data you are to use the run_script command where the number of nodes selected is set to the number of MPI processes that are employed. After this compare these execution times with that of the original serial program. What is the relative speedup and efficiency for each case? Is there a significant difference between the various parallel implementations? If so give a possible explanation as to why the execution time was not the same for each case given that the total number of threads is the same in all cases and your code was designed to evenly distribute the workload among the threads.

Execution times:
1 Process, 1 Thread - 889.82942 seconds
1 Process, 8 Threads – 244.24643 seconds
2 Processes, 4 Threads - 121.79133 seconds
4 Processes, 2 Threads - 116.63394 seconds
8 Processes, 1 Thread - 113.54748 seconds

Speedup:
1 Process, 1 Thread – 1.0
1 Process, 8 Threads – 3.64
2 Processes, 4 Threads – 7.31
4 Processes, 2 Threads – 7.63
8 Processes, 1 Thread – 7.84

Efficiency:
1 Process, 1 Thread – 1.0
1 Process, 8 Threads – 3.64
2 Processes, 4 Threads – 3.65
4 Processes, 2 Threads – 1.91
8 Processes, 1 Thread – 0.98

There is a pretty significant difference in runtime between the parallelized tasks. This could be due to collisions in memory access within a single multi threaded process. Each MPI process receives its own copy of the matrix elements, but the threads are operating on shared memory within their parent process.

Makefile:
all: mm_mult_hybrid mm_mult_serial_gnu

mm_mult_serial_gnu:
g++ src/mm_mult_serial.cpp -o bin/mm_mult_serial_gnu -O3

mm_mult_omp:
g++ src/mm_mult_omp.cpp -o bin/mm_mult_omp -O3 -fopenmp -Wall

mm_mult_hybrid:
export OMPI_CXX=g++
mpic++ src/mm_mult_hybrid.cpp -o bin/mm_mult_hybrid -O3 -fopenmp -Wall

clean:
rm bin/*
rm src/*.o

Source:
/******************************************************************/
/* Matrix Matrix Multiplication Program Example -- hybrid version */
/* September 2015 -- B. Earl Wells -- University of Alabama */
/* in Huntsville */
/******************************************************************/

/**
 * Christopher Bero
 * CPE 412
 * Homework 5
 */

using namespace std;
#include <iostream>
#include <iomanip>
#include <sstream>
#include <stdlib.h>
#include <string.h>
#include <sys/time.h>

/**
 * headers for an MPI/OMP program
 */
#include <mpi.h>
#include <stdio.h>
#include <stdlib.h>
#include <unistd.h>
#include <math.h>
#include <omp.h>

#define DEBUG false	/* whether to output matrices or not */
#define MX_SZ 320
#define SEED 2397 /* random number seed */
#define MAX_VALUE 100.0 /* maximum size of array elements A, and B */

/* copied from mpbench */
#define TIMER_CLEAR (tv1.tv_sec = tv1.tv_usec = tv2.tv_sec = tv2.tv_usec = 0)
#define TIMER_START gettimeofday(&tv1, (struct timezone*)0)
#define TIMER_ELAPSED ((tv2.tv_usec-tv1.tv_usec)+((tv2.tv_sec-tv1.tv_sec)*1000000))
#define TIMER_STOP gettimeofday(&tv2, (struct timezone*)0)
struct timeval tv1,tv2;

typedef struct matrix_dimensions
{
/**
* Corresponding:
* [l,m] * [m,n] = [l,n]
*/
unsigned int l, m, n;
} matrix_dimensions;

/**
 * Generic function which does the same as the definition statements
 */
float * cartesian (float * matrix, int row_sz, int row, int col)
{
return( (matrix + (row * row_sz) + col) );
}

/*
   Routine to retrieve the data size of the numbers array from the
   command line or by prompting the user for the information
*/
void get_index_size(int argc, char *argv[], unsigned int * tcount, unsigned int *dim_l, unsigned int *dim_m, unsigned int *dim_n)
{
    if(argc!=3 && argc!=5)
    {
        cout<<"usage: mm_mult_hybrid [thread_count] [l_dimension] <m_dimension n_dimmension>"
        << endl;
        exit(1);
    }
    else
    {
        if (argc == 3)
        {
        *tcount = atoi(argv[1]);
        *dim_l = *dim_n = *dim_m = atoi(argv[2]);
        }
        else
        {
        *tcount = atoi(argv[1]);
        *dim_l = atoi(argv[2]);
        *dim_m = atoi(argv[3]);
        *dim_n = atoi(argv[4]);
        }
    }
    if (*dim_l<=0 || *dim_n<=0 || *dim_m<=0 || *tcount <= 0)
    {
        cout<<"Error: number of rows and/or columns must be greater than 0"
        << endl;
        exit(1);
    }
}

/*
   Routine that fills the number matrix with Random Data with values
   between 0 and MAX_VALUE
   This simulates in some way what might happen if there was a
   single sequential data acquisition source such as a single file
*/
void fill_matrix(float *array,int dim_m,int dim_n)
{
    int i,j;
    for(i=0; i<dim_m; i++)
    {
        for (j=0; j<dim_n; j++)
        {
        array[i*dim_n+j]=drand48()*MAX_VALUE;
        }
    }
}

/*
   Routine that outputs the matrices to the screen
*/
void print_matrix(float *array,int dim_m,int dim_n)
{
    int i,j;
    for(i=0; i<dim_m; i++)
    {
        for (j=0; j<dim_n; j++)
        {
        cout << array[i*dim_n+j] << " ";
        }
        cout << endl;
    }
}

/*
pThreads worker commands
*/
void worker (float * local_a, float * b, float * c, unsigned int groupSize, \
long unsigned int mStart, matrix_dimensions dim, int vDisps[], int rank, unsigned int * tcount)
{
unsigned int i;
//cout << "rank: " << rank << ", tcount: " << *tcount << endl;
//fflush(stdout);
#pragma omp parallel for num_threads(*tcount)
for (i=0; i < groupSize; ++i)
{
long unsigned int elem = (mStart + i);
int a_row = (elem/dim.n);
int a_row_local= a_row - (vDisps[rank]/dim.m);
int b_col = (elem % dim.n);
float dot_prod = 0.0;
unsigned int k;

for (k=0; k<dim.m; k++)
{
dot_prod += *cartesian(local_a, dim.m, a_row_local, k) * *cartesian(b, dim.n, k, b_col); // A(a_row,k)*B(k,b_col);
}
c[i] = dot_prod;
}
}

/*
   MAIN ROUTINE: summation of a number list
*/
int main( int argc, char *argv[])
{
// Matrix variables
float *a,*b,*c;	/* matrix (0,0) address */
float * local_a;	/* chunk of a to operate on */
    matrix_dimensions dim;	/* matrix dimensions */
    long unsigned int i;	/* indexes */
long unsigned int mStart, mEnd;	/* index of beginning and ending elements for subproblem */
long unsigned int aCount, bCount, cCount;	/* Number of elements in matrix */
unsigned int * tcount;

// MPI variables
int nmtsks, rank;	/* default MPI variables */
unsigned int groupSize;	/* Number of elements to process */

/**
* MPI initialization
*/
MPI_Init(&argc,&argv);	/* initalize MPI environment */
MPI_Comm_size(MPI_COMM_WORLD,&nmtsks);	/* find total number of tasks */
MPI_Comm_rank(MPI_COMM_WORLD,&rank);	/* get task identity number */

tcount = new (nothrow) unsigned int;

    /**
     * Process 0 sets up the operands
     */
    if (rank == 0)
{
/*
get matrix sizes AND THREAD COUNT
*/
get_index_size(argc,argv,tcount,&dim.l,&dim.m,&dim.n);

aCount = (dim.l * dim.m);
bCount = (dim.m * dim.n);
cCount = (dim.l * dim.n);

// dynamically allocate from heap the numbers in the memory space
// for the a,b, and c matrices
a = new (nothrow) float[dim.l*dim.m];
b = new (nothrow) float[dim.m*dim.n];
if(a==0 || b==0)
{
cout <<"ERROR: Insufficient Memory" << endl << flush;
exit(1);
}

/*
  initialize numbers matrix with random data
*/
srand48(SEED);
fill_matrix(a,dim.l,dim.m);
fill_matrix(b,dim.m,dim.n);

/*
 output numbers matrix
*/
if (DEBUG)
{
cout << "A matrix =" << endl;
print_matrix(a,dim.l,dim.m);
cout << endl;

cout << "B matrix =" << endl;
print_matrix(b,dim.m,dim.n);
cout << endl;
}

// Start recording the execution time
TIMER_CLEAR;
TIMER_START;
}

/**
* Disseminate matrix dimensions and operands
*/
MPI_Bcast(&dim, (sizeof(dim)/sizeof(unsigned int)), MPI_UNSIGNED, 0, MPI_COMM_WORLD);
if (rank != 0)
{
aCount = (dim.l * dim.m);
bCount = (dim.m * dim.n);
cCount = (dim.l * dim.n);
b = new (nothrow) float[bCount];
if(b==0)
{
cout <<"ERROR: Insufficient Memory" << endl << flush;
exit(1);
}
}
MPI_Bcast(b, bCount, MPI_FLOAT, 0, MPI_COMM_WORLD); /* Every process gets a full copy of b */
MPI_Bcast(tcount, 1, MPI_UNSIGNED, 0, MPI_COMM_WORLD);

/**
* Calculate subproblem indexes
*/
groupSize = (cCount / nmtsks);
mStart = (groupSize * rank);
mEnd = (mStart + groupSize) - 1;

/**
* If we're the last proc,
* extend the group to any missed elements
*/
if (rank == (nmtsks-1))
{
mEnd = (cCount-1);
groupSize = (mEnd+1) - mStart;
}

/**
* Send only rows of matrix a that are needed
* A 5000x5000 matrix is 25000000 elements
* which with float is 100,000,000 bytes.
* I'm suddenly a little memory conscious.
*
* Need two arrays for scatterv:
* - Starting element in matrix a to send
* - Length of segment from matrix a to send
*/
int vSizes[nmtsks]; /* Size of segment */
int vDisps[nmtsks]; /* Offset of segment from 0 */
int elemStart, elemEnd;
unsigned int rootPartialA = (aCount / nmtsks); /* is the same for rank 0->(n-2) */
unsigned int lastPartialA = (aCount - (rootPartialA * (nmtsks-1)));
for (i=0; i< (unsigned int)nmtsks; ++i)
{
elemStart = ((i*rootPartialA))/dim.m*dim.m;
if (i == (unsigned int)(nmtsks-1))
{
elemEnd = ((((i*rootPartialA)-1)+rootPartialA)/dim.m)*dim.m + (dim.m-1);
} else {
elemEnd = ((((i*rootPartialA)-1)+lastPartialA)/dim.m)*dim.m + (dim.m-1);
}
vSizes[i] = (elemEnd - elemStart) + 1;
vDisps[i] = (elemStart);
}

local_a = new (nothrow) float[vSizes[rank]];
if(local_a==0)
{
cout <<"ERROR: Insufficient Memory" << endl << flush;
exit(1);
}

MPI_Scatterv(a, vSizes, vDisps, MPI_FLOAT, local_a, vSizes[rank], MPI_FLOAT, 0, MPI_COMM_WORLD);

/**
* Create resulting matrix
* Trying to save a little bit of memory on matrix C.
*/
if (rank == 0)
{
c = new (nothrow) float[dim.l*dim.n];
}
else
{
c = new (nothrow) float[groupSize];
}
if (c == 0)
{
cout <<"ERROR: Insufficient Memory" << endl << flush;
exit(1);
}

//cout << "MAIN rank: " << rank << ", tcount: " << *tcount << endl;
worker(local_a, b, c, groupSize, mStart, dim, vDisps, rank, tcount);

MPI_Status status;
if (nmtsks > 1)
{
if (rank == 0)
{
for (int mpitask = 1; mpitask < (nmtsks-1); ++mpitask)
{
MPI_Recv(&c[groupSize*mpitask], groupSize, MPI_FLOAT, mpitask, 123, MPI_COMM_WORLD, &status);
}
MPI_Recv(&c[groupSize*(nmtsks-1)], groupSize+(cCount % nmtsks), MPI_FLOAT, nmtsks-1, 123, MPI_COMM_WORLD, &status);
} else {
MPI_Send(c, groupSize, MPI_FLOAT, 0, 123, MPI_COMM_WORLD);
}
}

/**
* Proc 0 outputs results
*/
MPI_Barrier(MPI_COMM_WORLD);
    if (rank == 0)
{
/*
  stop recording the execution time
*/
TIMER_STOP;

if (DEBUG)
{
cout << "C matrix =" << endl;
print_matrix(c,dim.l,dim.n);
}
cout << endl;
cout << "time=" << setprecision(8) << TIMER_ELAPSED/1000000.0
<< " seconds" << endl;
}

MPI_Finalize();

return(0);
}