Since Canvas doesn't support MATLAB .m files

% HW1 - Problem 1
% Christopher Bero
% CPE 381

% Store 80 Minutes
store_minutes = 80;
seconds_per_minute = 60;

% a)
sample_hz = 8000;
bits_sample = 8;
space_a = sample_hz*bits_sample*store_minutes*seconds_per_minute;

% b)
sample_hz = 44100; % 44.1K Hz sampling frequency
bits_sample = 8; % 8 bits per sample
tracks = 2; % stereo
space_b = sample_hz*bits_sample*tracks*store_minutes*seconds_per_minute;

% c)
space_c = (space_b / 20.0);

% d)
video = (640 * 480);
colors = 3;
bits_color = 8;
sample_hz = 30;
space_d = (video*colors*bits_color*sample_hz*seconds_per_minute*store_minutes);

% HW1 Problem 2
% Christopher Bero
% CPE 381

% Setup x axis and sampling rate
p2_x_a = 0:0.0001:3;
p2_x_t01 = 0:0.1:3;
p2_x_t05 = 0:0.5:3;
p2_x_t10 = 0:1.0:3;

% Setup y(x)
p2_y_a = (2*cos(p2_x_a*2*pi));
p2_y_t01 = (2*cos(p2_x_t01*2*pi));
p2_y_t05 = (2*cos(p2_x_t05*2*pi));
p2_y_t10 = (2*cos(p2_x_t10*2*pi));

% Plot all y(x)
figure('Name', 'This is indeed a figure', 'NumberTitle', 'off')
subplot(2,2,1);
plot(p2_x_a, p2_y_a);
hold all
%stem(p2_x_a, p2_y_a);
xlabel('x(t)');
ylabel('y()');
title('analog');

subplot(2,2,2);
plot(p2_x_a, p2_y_a);
hold all
stem(p2_x_t01, p2_y_t01);
xlabel('x(t)');
ylabel('y()');
title('T=0.1');

subplot(2,2,3);
plot(p2_x_a, p2_y_a);
hold all
stem(p2_x_t05, p2_y_t05);
xlabel('x(t)');
ylabel('y()');
title('T=0.5');

subplot(2,2,4);
plot(p2_x_a, p2_y_a);
hold all
stem(p2_x_t10, p2_y_t10);
xlabel('x(t)');
ylabel('y()');
title('T=1.0');

% Analog information lost after Ts=0.5 sec.

% HW1 Problem 3
% Christopher Bero
% CPE 381

% MATLAB instructs me to replace i and/or j with (1i).

p3_z = (1+((1i)*1));
p3_w = exp(p3_z);

p3_a=log(p3_w);
% 1.000000000000000 + 1.000000000000000i

% b)
% real: 1.0
% imag: 1.0i

p3_c=p3_w+(conj(p3_w));
% 2.937387879831771

p3_d1=abs(p3_w);
% 2.718281828459046

p3_d2=angle(p3_w);
% 1

p3_e=square(abs(log(p3_w)));
% 1

% f)
% e^(j1) = (cos(1) + jsin(1))
% (x^2)*(x^3) = x^5 = x^(2+3)
% w = (e^(1+j1)) = (e^(1) * e^(j1))
% w = e^(1)*(cos(1) + jsin(1))
% (cos(1) + jsin(1)) = w/(e^(1))
% cos(1) = w/(e^1) – jsin(1)

% problem 5

A=1.0;
Omega=(2*pi);

x_axis=-3:0.01:3;

y_t=A*sin(Omega*x_axis);

x_t=A*cos(Omega*x_axis);

z_t=y_t + x_t;

plot(x_axis, y_t);
hold all
plot(x_axis, x_t);
hold all
plot(x_axis, z_t);

% p4_a
% Yes, the graph shows how a phasor will allow the functions to act
% interchangeably. It would take -(pi/2) radians to shift sine to match
% cosine.

% p4_b
% The phasor for z_t is -(pi/4) to relative to cosine

% problem 7

x_axis=-10:0.1:10;

x_t = exp(-(abs(x_axis)));
abs_x_t = abs(x_t);

%plot(x_axis, x_t);
%hold all
%plot(abs_x_t);
%hold all
%plot(square(abs_x_t));

% p7_a
% The integral is infinite because the function is based upon e^(x).

% p7_c
y_t = exp(-x_axis)*cos(2*pi*x_axis)*x_t;
plot(x_axis, y_t);

% problem 8

x_axis = -5:0.01:5;

x_t = cos(2.*2.*pi.*x_axis) + 2.*cos(2.*pi.*x_axis);

plot(x_axis, x_t);

% a)
% T0 = 1s

% from pg 85
fun = @(x) square(cos(2.*2.*pi.*x) + 2.*cos(2.*pi.*x));
q = (1/(1))*integral(fun, 0, 1);

% b)
% P(q) = -0.238563468046797

fun_a = @(x) square(cos(2.*pi.*x));
q_a = (1/(1))*integral(fun_a, 0, 1);

% q_a = 1.613811758020811e-11

fun_b = @(x) square(cos(2.*cos(pi.*x)));
q_b = (1/(1))*integral(fun_b, 0, 1);

% q_b = 0.150167170794685

% P(q) != q_a + q_b

% HW1 problem 9
% Christopher Bero

x_axis = -5:0.01:5;

x_1t = (4*cos(pi*x_axis));

x_2t = (-sin((3*pi*x_axis)+(pi/2)));

plot(x_axis, x_1t); % a) T1t=2s
hold all
plot(x_axis, x_2t); % a) T2t=0.66s
hold all
plot(x_axis, (x_1t + x_2t)); % b) yes, Txt=2s

%p9_c: T=12

%p9_d:
x_1t = (4*cos(2*pi*x_axis));
x_2t = (-sin((3*pi*x_axis)+(pi/2)));
hold all
plot(x_axis, (x_1t + x_2t)); % yes

x_1t = (4*cos(2*x_axis));
x_2t = (-sin((3*pi*x_axis)+(pi/2)));
hold all
plot(x_axis, (x_1t + x_2t)); % yes