Lab 07
Christopher Bero
EE384

Problem 1

function [ tone, fs ] = dtmfdial( keys )
% dtmfdial - Phone a friend
% Input - 1x? matrix of keys pressed 1-12, such as [1 3 5 9 11 12]
% Output - Audio at 8kHz, sampling frequency

% DTMF
% ___________________________
% | Freq | 1209 | 1336 | 1477 |
% | 697 | 1 | 2 | 3 |
% | 770 | 4 | 5 | 6 |
% | 852 | 7 | 8 | 9 |
% | 941 | *(11)| 0(10)| #(12)|
% |______|______|______|______|

% Variables
fs=8000; % Sampling frequency
td=0.5; % Tone duration
sd=0.1; % Space duration
cols=[1209 1336 1477];
rows=[697 770 852 941];
len=0;
tone=zeros(1,(length(keys))*fs*0.6); % Initialize sound vector

% for every button listed in the input vector
for button = keys
    % Fix the keymapping so that buttons are sequential
    if button == 10
        button = 11;
    elseif button == 11
        button = 10;
    end
    % Get row and column index
    col_index=mod((button-1),3)+1;
    row_index=int8(ceil(button/3));

    % Use indecies to get frequency
    freq1=cols(col_index);
    freq2=rows(row_index);

    % Create time vectors
    t=0:(1/fs):td;

    % Generate the button's sound
    touch_tone=sin(2*pi*t*freq1)+sin(2*pi*t*freq2);
    silence=zeros(1,(sd*fs));

    % Append to output
    tone((len+1):(len+length(t)+length(silence)))=[touch_tone silence];
    len=(len+length(t)+length(silence));
end

%plot(tone);

% Splicing example
% tone(24005:24006) = [20 21];

end

Problem 2

function [ keys ] = dtmfdecode( tone, fs )
% dtmfdecode - Receiving end for dtmfdial()
% input - 1x? audio matrix, sampling frequency
% output - 1x? matrix of key values

% This function could be built to take 0.6 second chunks at a time
% since we know where the audio is coming from.
% I'm going to try to make it more robust though, so that the audio
% can be shifted in the incoming signal.
% To do this, I plan to check 0.05 second chunks since the smallest
% audio (silence) is 0.1s. So we're employing Nyquist's Frequency
% to make sure that the silence is noticed. Then we'll parse the
% incoming signal by using silence as a cue to move on to the
% next button tone.

% DTMF
% ___________________________
% | Freq | 1209 | 1336 | 1477 |
% | 697 | 1 | 2 | 3 |
% | 770 | 4 | 5 | 6 |
% | 852 | 7 | 8 | 9 |
% | 941 | *(11)| 0(10)| #(12)|
% |______|______|______|______|

% Variables
rd=0.05; % Reference duration
cols=[1209 1336 1477];
rows=[697 770 852 941];
keys_list=[1 2 3; 4 5 6; 7 8 9; 11 10 12];
len=length(tone);
keys_index=1;
%keys=[];
prev_f=0;

% States
% 1 - Consuming silence
% 2 - Stacking tone chunks
state=2;

prev_sig=zeros(1,rd*fs);
prev_power=sum(prev_sig);
stacked_sig=zeros(1,len-1);

for section = 0:1:uint16(floor( ( (len)/fs )/rd )-1)
    this_sig=tone( ((section*fs)*rd)+1 : ((section+1)*fs)*rd );
    [p_vals,p_sig]=powerSpec(this_sig,fs);
    %plot(p_vals,p_sig);
    %hold on;
    stacked_sig( ((section*fs)*rd)+1 : ((section+1)*fs)*rd ) = this_sig;
    p_power=sum(abs(p_sig));

    % State 1
    if state == 1
stacked_sig=zeros(1,len-1);
if p_power > (prev_power*3)
%disp('Found signal');
state=2;
end

end

    % State 2
    if state == 2
        if p_power < (prev_power/3)
        %disp('Found silence');
        state=1;

        [stacked_vals,stacked_p]=powerSpec(stacked_sig,fs);
        max_col_range=find(stacked_vals>1109&stacked_vals<1577);
        max_row_range=find(stacked_vals>597&stacked_vals<1041);
        [C,I]=max(stacked_p(max_col_range));
        col_button_freq=floor(stacked_vals(I+(min(max_col_range)-1)));
        [C,I]=max(stacked_p(max_row_range));
        row_button_freq=floor(stacked_vals(I+min(max_row_range)-1));

        col_index=find(cols>(col_button_freq-10) & cols<(col_button_freq+10)); %mod((button-1),3)+1;
row_index=find(rows>(row_button_freq-10) & rows<(row_button_freq+10)); %int8(ceil(button/3));
        keys(keys_index)=keys_list(row_index,col_index);
        keys_index=keys_index+1;
        else

        end
    end

    prev_power=p_power;
end

end