Christopher Bero
6-2-2015
CPE 324

Lab Report 03

Design Capture and FPGA-based Rapid Prototyping using the DE2-115 Platform
(Implementation of an 8-bit Subtractor/Adder)

Introduction
In this lab we will learn how to operate Quartus for synthesis of a Structural and Verilog projects. We will load the synthesized combinational logic to the DE2-115 and test directly, rather than simulate with stimulus inputs. The lab will then analyze the multiple synthesis and implementations to determine any differences between the design techniques. It is my personal goal to learn about Quartus so that I may be best prepared to generate a better FPGA interface at some point in the future, as highlighted by the general user interface shortcomings of Quartus below.
Though general synthesis and simulation of Verilog is possible with libre tools such as icarus, the fragmentation of the commercial scene makes implementing a system without proprietary software nontrivial. If one currently wishes to compile and simulate Verilog for a Cyclone-IV-E FPGA chip, the only answer I can provide is Altera's own Quartus toolkit, and this trend appears to hold for most other major FPGA manufacturers, though Xilinx does seem to work toward an open source toolchain. FPGA's receive special interest from me because they act as a bridge otherwise ignored by higher education. Classes at this campus range from high level operating system architecture to physical analysis of logic elements, but either due to interdepartmental miscommunication or direct apathy do not provide a solid basis of understanding for computer design to students. Instead we are left to make the transition from “computers are magic” to “computers are tiny pieces” to “computers are incredibly small gates flashed onto a wafer of silicon by a laser which makes gigantic systems of millions of parts that all work together at speeds we cannot comprehend to support a modern operating system” on our own whim.
Fortunately, FPGAs provide a high level system that can be directly represented as discrete logic elements. This juxtaposition allows us students to move forward where the institution would otherwise leave us ignorant. So it is for the purpose of eventually progressing the realm of free and open source FPGA tools and devices, which may make future educational establishments more robust, that we conduct our lab today.

Theory and Analysis
Our lab consisted of combinational logic systems which had most reduction and design techniques resolved beforehand, leaving us to “plug and play” so to speak. The prelab assignment consisted of ensuring our familiarity with generating Verilog and Schematic projects in Quartus, which we were introduced to in Lab 02. For generating a test driver for our system, we use the following understanding of a binary adder and subtractor:

- Adding two number which do not generate a carry.
- Both numbers must sum to be less than the maximum value of our container. Since we have four bit containers, the maximum value is 15, or the 16th position in our counting scheme as determined by (2^4).
- Subtract two number which do not generate a borrow.
- A similar arrangement as the previous item, we must make sure that our two values do not subtract to become a value not found in our container. In this case our minimum value is zero, after which the container will continue counting as though an additional bit is supplied from a higher power of 2.
- Add/Subtract values which have a carry/borrow.
- As before, except we now prime the system with a carry in or borrow bit which will prompt the output to either be one digit higher or one digit lower.
- Propagate the carry or borrow bit from LSB to the output.
- This proved to be the most difficult task, as choosing the values required a better understanding of the system. Possible values were eventually chosen which would sum to 15, and with a carry in bit overflow to generate a carry out.
- Choose values which prompt an overflow into the carry bit or create a negative result.
- In this case we reverse our stance and attempt to force the values to exceed the container's representation, which will hopefully provoke the adder/subtractor to indicate the exception.

Procedures
During the generation of the Schematic project in Quartus, I had difficulty utilizing the program. Contrary to my intuition, Quartus will generate as many solid connections between two lines which cross as possible. This results in a much longer design timeframe in which every line must be broken down into multiple sections that are carefully routed around nearby lines. An example is as follows:

Illustration 1: Lines Incorrectly Merged
This does not appear to be discussed in the lab manuals or Quartus guide, as such I am unsure if a configuration option has been overlooked which would instigate a more straightforward workflow.
During the pin assignment we did notice that the link between pin name and physical switch can be exported and reused to save time. To export a configuration in Quartus: from the Pin Planner, File->Export->Save as CSV. To reuse in Quartus: Assignments->Import Assignments, choose the CSV file.
Other procedures were followed as closely as possible from the lab manual, “Design Capture and FPGA-based Rapid Prototyping using the DE2-115 Platform”. The Schematic project was generated from images proved, which may have lead to naming discrepancies due to the provided image quality. Additionally, the screenshots which were not referenced until after the conclusion of the lab were not gathered, though lab project files are available at the request of the lab instructor or course professor.

Stimulus used:
- SUB_ADD[0] A[0011] B[0001] C_IN[0]
- SUB_ADD[1] A[0011] B[0001] C_IN[0]
- SUB_ADD[0] A[0011] B[0001] C_IN[1]
- SUB_ADD[1] A[0111] B[0001] C_IN[1]
- SUB_ADD[0] A[1111] B[1110] C_IN[1]
- SUB_ADD[1] A[1110] B[1110] C_IN[1]
- SUB_ADD[0] A[1111] B[1111] C_IN[0]
- SUB_ADD[1] A[0011] B[1001] C_IN[0]

Results
Part 1 – Schematic
Total Logic Elements: 8
Design operated correctly on the first attempt.

Part 2 – Verilog
Total Logic Elements for Structural: 16
Total Logic Elements for Behavioral: 18
Designs operated correctly on the first attempt.

Compile time for both representations: 42 seconds.

Conclusion and Discussion
The returned logic element count from Quartus does not pass a preliminary intuition test, and we counted on the level of 80 logic elements for the Schematic design, which only reported 8. This may be due to a misunderstanding of what is being reported, such as a logic element being represented in the same way an IC with nor gates is one element with a collection of gates.
During compilation we received several warnings pertinent to clock speed and pin assignment, though we could not determine any source to correct the issue, and the project appears to operate correctly. These warnings were present for all three projects. Schematic representation quickly became more difficult to manage in Quartus as the use of generic blocks eschewed the underlying operations. More interaction with the Verilog components of Quartus and general language is needed to generate a preference of analysis of the representations. The stimulus used in this lab was tertiary and should only be considered a basis for general implementation, input which tests the boundaries between carry_in, carry_out for both addition and subtraction should be implemented for a more robust trial of the design. As stated above, we're unsure that logic elements reported is an appropriate representation of FPGA resources being used, though if it is to be believed the Schematic representation is much more lightweight. Other than system resources required, both types of project compiled in similar time, leaving us with no hard preference for which system to give priority in the future.