Christopher Bero
3-4-2015
CPE 324

Lab Report 06

Capacitance Tester

Introduction

In this lab we explore the design of a hybrid digital/analog circuit capable of measuring the capacitance of a device within bounds. 555 timers are a very utilitarian component, capable of several modes of operation. We will employ a 555 timer in an astable multivibrator circuit for our capacitance meter. This will allow us to measure the time taken for a given capacitor to discharge, and from there determine its associated value. Two methods will be taken to programming the DE2-115 as a control and interpreter for the circuit. We will first work with a structural Verilog model which closely follows the physical representation of the circuit; then on a higher level behavioral Verilog model which is contained in a single module. By using these two approaches we hope to learn more about the distinction between various approaches to Verilog programming, and to appreciate the performance versus implementation impact on the FPGA.

Theory and Analysis

Our lab hinges on the workings of an RC circuit.

We know from previous experience with circuits that dQ(t)/dt = -(Q(t)/T which brings us to the exponential relationship: Q(t) = Qoe(-t/T) = Qmaxe(-t/RC). We also take analysis of our given implementation: Vs – Vr – Vc = 0; Vr/R + Ci = 0 → Vr/R + C(dVc/dt) = 0 by KVL and KCL. Since we are placing the capacitor in a controlled circuit, in which we wish to know the quantity of Voltage delivered over a period of time, we can adjust the implied focus of our equation from sum-of-charge to sum-of-voltage. From the previous equations and constants available in our circuit, we gather Vc + (5111)C(dVc/dt) = 0, with solution Vc – (Vci)e(-t/(5111)C). Given that the capacitor will be discharging from (2/3)Vcc to (1/3)Vcc, the solution to our differential equation becomes (1/3)Vcf = (2/3)(Vci)e(-t/(5111)C) which can be solved with t ~ 3543C. This value will allow us to approximate a range of capacitances by “counting” the number of 0.01uF instances which pass while discharging.

Procedures

Procedures were followed as closely as possible from the lab manual “CPE 324 Advanced Logic Design Laboratory – Capacitance Tester”. Some time was devoted to investigating the available templates for part 2 of the project, and the lab was ultimately carried out with template 3. Considerable time was invested for reviewing the assembled 555 timer based circuit, as the loaded operation of the Verilog occasionally differed wildly between instances. It was found that the breadboard used had several null connections which had metal contacts worn too far apart to hold a wire in place. Once fixed, the circuit and loaded program operated as expected.

Results

This lab indeed aided us in understanding structural and behavioral Verilog to a better degree. The method used for determining the capacitance of our object was foreign, but has made more sense as we take the extra time available to explore the Verilog implementation and provided documents. Our circuit was able to measure the capacitance of a capacitor to within several hundredths of a microfarad for all capacitors available.

Conclusion and Discussion

It is possible that the design approach understood from the assignment was misinterpreted, and that our Verilog only works for the correspondingly low capacitances tested against the circuit. This discrepancy would require a larger gamut of capacitances used in testing to be known, and is otherwise just speculation. At the conclusion of this lab, we wonder what other combinational or sequential logic elements could be used to efficiently replace the FPGA in displaying a capacitance, though without a provided clock source from either an FPGA or microcontroller a loss of precision would be expected.

Questions

1.
A 555 timer in multivibrator mode has two output states, stable and astable. Energy stored in a capacitor triggers the change in state as it reaches a threshold.

2.
Variability in the 10 KOhm resitor would only marginally affect a voltage divider associated with the latched output of the circuit; the 5.111 Kohm resistor directly affects the measured capacitance of our capacitor.

3.
count_enabler was modified to have a 16 bit counting space, and full_count was loaded from the associated value derived in “Theory and Analysis”.

4.
Without the flip-flop, the counter would not clear, and would instead iterate through its range of values rather than be set to our determined capacitance.

5.
The one-shot implementation keeps the 16 bit flip-flop from jumping multiple values while enabled.

6.
The behavioral design shared many characteristics with the previous structural design, but in practice followed the course of the association between the counter, bcd display, and 555 timer input rather than set modules which would accomplish the same task but refer to lower level designs.

7.
The structural implementation used 127 logic elements, 78 registers, 30 pins.
The part2 behavioral template used 111 logic elements, 58 registers, 30 pins.
I found the behavioral implementation easier to implement, as it more clearly follows the workflow generated to count instances of a capacitance. It was similarly surprising to see that it was also the more space efficient version as well.